## Slide 1: Warm magnets in point 3
M. Giovannozzi
The problem:
Due to the high circuit resistance, some magnets in IR3 are limited below the nominal or ultimate performance.
The solution consists in pulling additional cables in parallel to those already installed.
The issue is to specify which circuits should be modified.
Acknowledgements: G. Arduini, R. Assmann, R. Bailey, R. Saban, H. Thiesen.

## Slide 2: The “weak circuits”
RQT4/5 are the only circuits for which Imax < Inom
Ioperation refers to the optics with momentum collimation in IR3. De-tuned optics is less demanding in terms of strength.
The request is to modify only the circuits RQT4/5.
Offered to modify also RCBWH5.R3B1 and RCBWV5.R3B2.
The cable installation is not mandatory before the 2008 run.