| LHC- - - 1999-09-22 |
| --- |
| MPS Commissioning Procedure |
| The commissioning of the LHC machine protection system MPS aspects of the vacuum system commissioning |
| Abstract This document describes the set of tests which will be carried out to validate for operation the machine protection aspects of the LHC vacuum system. The area concerned by these tests extends over the whole LHC machine for each of the two LHC beams. These tests include the Hardware Commissioning, the machine check-out and the tests with beam. |
| Prepared by : Jean-Christian Billy Laurette Ponce Bruno Puccio Jan Uythoven | Checked by : Ralph Assmann, Roger Bailey Andy Butterworth Bernd Dehning, John Robert Etheridge Brennan Goddard, Eva Barbara Holzer, Miguel Jimenez Verena Kain, Mike Lamont, Isabelle Laugier Blanca Perea Solano Stefano Redaelli, Rudiger Schmidt, Benjamin Todd, Jorg Wenninger, Markus Zerlauth | Approved by : Rüdiger Schmidt |
| History of Changes |
| Rev. No. | Date | Pages | Description of Changes |
| 0.1 0.2 | 2007-02-16 2007–03-13 | 8 All | First draft for circulation. Reorganisation of the document and including many comments |

Table of Contents

1.	Introduction	4

2.	Scope	4

3.	Purpose	4

4.	The layout	4

5.	Tests performed during the hardware commissioning	5

5.1	Individual vacuum system tests	5

6.	Link to other equipement	6

6.1	IntErfaceS with the Beam Interlock system	6

6.2	interface with the rf system	7

6.3	interface With the MKI	8

6.4	interface with the MKB	8

6.5	interface with the MSD	8

6.6	interface with the access system	8

7.	System tests during the machine checkout	8

7.1	Conditions required to perform tests	8

7.2	Description of the tests	8

7.3	Status of the system after the system tests	9

8.	Tests with beam.	9

# Introduction

After the qualification for operation of the individual systems of a sector, validation and specific studies of each equipment as a whole will be carried-out in the context of the machine protection system (MPS) commissioning.

# Scope

This document covers the tests which will be carried-out to condition and validate for operation all the components of the vacuum system in relation with the machine protection system for LHC beam 1 and 2. The area concerned by these tests is the whole LHC ring and the beam dump lines TD62 and TD 68. The equipments concerned are the vacuum system, the beam interlock system, the LHC beam dump system (to be checked), etc….

# Purpose

This document

gives a comprehensive list of the components which will be the object of the tests (sector valves, BIC, gauges).

describes in detail the procedures which will be applied for these tests and their sequence.

Each test has in front one of the following letters, defining at which interval or at which occasion the described test needs to be repeated (in the column labelled Repetition):

| N | Not to be repeated |
| --- | --- |
| S | To be repeated after every Shutdown |
| P | Periodical repetition required, like 1 x per month; details to be defined in text |
| O | To be repeated when LHC optics is changed |
| X | To be repeated when crossing scheme is changed |

This document is meant to be the reference document for the checklist which will be used during the commissioning of the MPS. Results of the tests will be documented in the MTF database.

# The layout

The LHC ring vacuum system is comprised of 4 sub-systems: the two independent beam pipes, the isolation vacuum in the cryostat and the cryoline. For the four systems, the material installed in the LHC is around:

300 sector valves for the beam vacuum;

200 fix pumping stations and 150 mobile stations;

800 gauges;

1300 ionic pumps;

300 PLCs;

A schematic layout of the Beam vacuum system is shown schematically in Fig. 1. It is worth to note that there is no sector valve within the continuous cryostat between Q7R and Q7L: the octant arc is only one vacuum sector.

Figure 1: Schematic layout of the sector valves positions in LSS1L.

In each LHC beam dump line there are two vacuum valves (VVGSH.682980.B1, VVGSH.683178.B1, VVGSH.622980.B2, VVGSH.623178.B2) which will also need to be tested.

The closure of a sector valves takes about 3 – 4 seconds (check!)

# Tests performed during the hardware commissioning

This part describes the tests which are validated during the equipment’s hardware commissioning period and have to be validated also for the machine protection system commissioning.

## Individual vacuum system tests

Independent test of each sector valve will be made by AT/VAC.

The tests will be grouped for each half sector and for the beam dump lines TD62 and TD68.

### Conditions required to perform tests

Installation completed in one half-sector

Beam_Info signal from the BIS bypassed

### Conditions during the tests

Visual check of the closure of the valves is needed in situ and the closure of the valve can only be done locally.

### Description of the tests

|  | Rep. | Action | Group(s) Responsible |
| --- | --- | --- | --- |
| 1 | S | For each individual sector valve in the sector check the closure by ….. put details on how closure is forced | AT/VAC |
| 2 | S | For each individual sector valve check that the User_Permit is changed by the movement of a sector valve | AT/VAC |
| 3 | S | For each “group” of gauges check that the User_Permit is changed by pressure over threshold of 3 out of 4 or 2 out of 3 gauges | AT/VAC |

### Status of the system after tests

After these tests, the logic of the interlocks has been checked and the system is ready to be tested with the beam interlock system.

# Link to other equipement

The interfaces listed in this paragraph concern only the ones in relation with the Machine Protection System; it does not describe any procedures to test the interfaces to protect individual equipment but only summarise the logic applied in the design.

No details of tests are described in this section. Reference to tests, described for the equipment being linked to, is made when required.

## IntErfaceS with the Beam Interlock system

### SIGNALS between vacuum SYSTEM and Beam INTERLOCK SYSTEM

The vacuum system produces an interlock from each sector valve, concentrated for each half octant ??? in 16 signals for each beam sent to the beam interlock system (BIS). The interlocks generated by the intersection regions valves are concentrated in 6 double signals.

The “Beam_Info” signal given by the BIS is used in order to ensure that there is no beam before closing a sector valve.

The sector valves in the dump lines are interlocked in the same way as the ring valves: where is this valve? Separate to tests per half sector – separate listing!

### Conditions and sequence for a beam dump

The vacuum User_Permit signal is set to “TRUE” if all the sector valves are open. The “OPEN” status is given by contact of a single hardware switch and the signal is divided for redundant transmission to the BIS. The signal is changed to “FALSE” in case of:

A valve is closing or moving (status = NOT OPEN which trigs the User_Permit to false).

The pressure read at three out of four gauges within a sector is larger than the threshold (10-11 mbar).

If one of the two previous conditions is fulfilled, vacuum system changes its User_Permit from “TRUE” to “FALSE”, then the BIS changes the Beam_Permit from “TRUE” to “FALSE” to make the beam extracted by the beam dump system.

The BIS then changes the Beam_Info signal from “TRUE” to FALSE” and the vacuum system uses this signal to close the sector valve if necessary.

Figure 2: Sequence for a beam dump request from the vacuum interlock.

### Conditions required to perform tests

To perform these tests the following conditions are required:

The VME Beam Interlock Controllers must be installed in the tested octant.

Tested, verified software is needed for the BIC.

### Description of the tests

The tests are described in more details in the procedures of BIS commissioning (Note B. Puccio…)

|  |  | Action | Group(s) Responsible |
| --- | --- | --- | --- |
| 1 | S | Check that the User_Permit signals from vacuum system is correctly received by the all the BICs | AB/CO AT/VAC |
| 2 | S | Check that the Beam_Info signal send by the BIS after the beam dump is correctly received by the vacuum system | AB/CO AT/VAC |
| 3 | S | Change the threshold to generate an interlock and check that the valve does not move before the Beam-Info signal from the BIS is received | AB/CO AT/VAC |
| 4 | S | Check that the closure on a valve on Beam 1 is dumping beam 1 (exact procedure to de defined?) | AB/CO AT/VAC |
| 5 | S | Check that the closure on a valve on Beam 2 is dumping beam 2 (exact procedure to de defined?) | AB/CO AT/VAC |
| 6 | S | Check that the closure of a valve common to both beam is dumping both beam. | AB/CO AT/VAC |
|  |  | … |  |

## interface with the rf system

The vacuum system is giving two interlock signals, one digital and one analogue, directly to the RF system in order to either stop the High voltage or stop the RF enable.

For nominal intensity, the beam becomes unstable if one cavity is off, and it is then plan to have a hardware interlock to dump the beam. The exact conditions of triggering the beam dump have still to be defined based on first year experience with beam. Anyway, at low intensity, the beam can stand the loss of one cavity and a beam dump is not necessary. Therefore, no beam dump request related to the RF vacuum status will be implemented for LHC commissioning.

## interface With the MKI

The vacuum system is giving two interlock signals, one digital and one analogue, directly to the MKI system in order to either stop the High voltage or stop the pulse enable, and inhibit the injection permit.  In this case, the two beam pipes are linked from the point of view of the vacuum: the 4 sectors valves around each MKI are closed in case of a vacuum leak.

These interlocks concern the equipment protection and not the Machine Protection System.

## interface with the MKB

There is an interlock from the vacuum to stop the kickers in case of pressure over a threshold and a beam dump request is sent directly to the LBDS. This is an internal interlock to the LBDS system which will be tested at the level of the individual equipment tests. (to be confirmed by Etienne Carlier)

## interface with the MSD

To be completed

## interface with the access system

The beam stoppers are seen as sector valves by the vacuum system. (Logic of the interlock has to be checked with the INB regulation).

# System tests during the machine checkout

After the Individual System Tests, described in the previous sections, have been successfully completed, the integral system should be tested from the CERN Control Centre (CCC), simulating as much as possible future operation with beam.

## Conditions required to perform tests

Successful completion of the individual tests of the vacuum system sector by sector.

Successful completion of the tests mentioned in the previous sections.

Logging system available

BIS operational

LBDS operational

## Description of the tests

The tests have to be performed for sets of 3 or 4 gauges and 3 sector valves per beam and per octant. They will also need to be tested for the four vacuum valves located in the two beam dump lines.

Details of measuring delays remains to be sorted out with JC Billy!

|  |  | Action | Group(s) Responsible |
| --- | --- | --- | --- |
| 1 | S | Test beam dump request of the correct beam triggered by pressure over threshold for each octant: generate interlock at the level of a sector valve by changing the interlock threshold for 2 out of 3 signals Measure the delay between detection of “vacuum over threshold” and the beam dump request Measure the delay between the beam dump request and detection of status “NOT OPEN” of the sector valve | AB/CO AB/BT AT/VAC |
| 2 | S | Test the beam dump request of the correct beam triggered by the closure of a sector valve for each octant: Generate interlock by closing a sector valve Measure the delay between detection of satatus “NOT OPEN” and the beam dump request | AB/CO AB/BT AT/VAC |

## Status of the system after the system tests

After these tests, the machine protection aspects of the vacuum system have been validated for an arbitrary chosen element for each octant.

# Tests with beam.

There is no requirement to perform tests with beam.

The test to send a low intensity beam on a vacuum valve and ‘calibrate’ the BLM signals can be part of an MD. It will not be a test required tooperate with beam above a certain intensity.

# Text boxes

Beam_Info

Beam_Permit

LBDS

User_Permit

BIS

Vacuum