Staged commissioning of high luminosity operation of LHC at points 1 and 5

| Machine parameters | 450GeV | Commission hardware for high energy operation | Stage I | Stage II | Stage III | Installation of phase II collimators and full beam dump diluters | Stage IV |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Target |  | Target | Limit | Target | Limit | Target | Limit |  | Target | Limit |
| spacing | ns | 2021 |  | 2021 | 566 | 75 | 75 | 25 | 25 |  | 25 | 25 |
| bunch length | m | 0.1124 |  | 0.0755 | 0.0755 | 0.0755 | 0.0755 | 0.0755 | 0.0755 |  | 0.0755 | 0.0755 |
| crossing angle | urad | 0 |  | 0 | 0 | 250 | 250 | 285 | 285 |  | 285 | 285 |
| bunch intensity |  | 4.00E+10 |  | 4.00E+10 | 9.00E+10 | 4.00E+10 | 9.00E+10 | 5.00E+10 | 5.00E+10 |  | 9.00E+10 | 1.15E+11 |
| bunches |  | 43 |  | 43 | 156 | 936 | 936 | 2808 | 2808 |  | 2808 | 2808 |
| energy | eV | 4.50E+11 |  | 7.00E+12 | 7.00E+12 | 7.00E+12 | 7.00E+12 | 7.00E+12 | 7.00E+12 |  | 7.00E+12 | 7.00E+12 |
| F |  | 1.00 |  | 1.00 | 1.00 | 0.96 | 0.92 | 0.90 | 0.84 |  | 0.90 | 0.84 |
| normalised emittance | cm | 3.75E-04 |  | 3.75E-04 | 3.75E-04 | 3.75E-04 | 3.75E-04 | 3.75E-04 | 3.75E-04 |  | 3.75E-04 | 3.75E-04 |
| beta* | cm | 1100 |  | 200 | 200 | 200 | 100 | 100 | 55 |  | 100 | 55 |
| luminosity | /cm2s | 7.16E+28 |  | 6.12E+30 | 1.12E+32 | 1.28E+32 | 1.24E+33 | 1.13E+33 | 1.91E+33 |  | 3.65E+33 | 1.01E+34 |
| total inel cross section | cm2 | 6.00E-26 |  | 6.00E-26 | 6.00E-26 | 6.00E-26 | 6.00E-26 | 6.00E-26 | 6.00E-26 |  | 6.00E-26 | 6.00E-26 |
| event rate per cross |  | 0.01 |  | 0.76 | 3.85 | 0.73 | 7.09 | 2.14 | 3.63 |  | 6.94 | 19.18 |
| protons per beam |  | 1.72E+12 |  | 1.72E+12 | 1.40E+13 | 3.74E+13 | 8.42E+13 | 1.40E+14 | 1.40E+14 |  | 2.53E+14 | 3.23E+14 |
| current per beam | mA | 3.09E+00 |  | 3.09E+00 | 2.53E+01 | 6.74E+01 | 1.52E+02 | 2.53E+02 | 2.53E+02 |  | 4.55E+02 | 5.81E+02 |
| energy per beam | Joules | 1.24E+05 |  | 1.93E+06 | 1.57E+07 | 4.19E+07 | 9.43E+07 | 1.57E+08 | 1.57E+08 |  | 2.83E+08 | 3.62E+08 |
| beam size | um | 293.3 |  | 31.7 | 31.7 | 31.7 | 22.4 | 22.4 | 16.6 |  | 22.4 | 16.6 |