| Target machine parameters - Engineering run - 450GeV |
| --- |
| Set parameters | Unit | Injection | Collision |
| Crossing angle 1 & 5 | μrad | 0 | 0 |
| Crossing angle 2 | μrad | 0 | 0 |
| Crossing angle 8 | μrad | 0 | 0 |
| Separation 1 & 5 | mm | 5 | 5 |
| Separation 2 | mm | 4 | 4 |
| Separation 8 | mm | 4 | 4 |
| Beta * 1 & 5 | m | 11 | 11 |
| Beta * 2 & 8 | m | 10 | 10 |
| Crossing plane 1 |  | - |
| Crossing plane 2 |  | - |
| Crossing plane 5 |  | - |
| Crossing plane 8 |  | - |
| Energy | TeV | 450 | 450 |
| Number of bunches |  | 43 |
| Bunch intensity |  | 4 1010 |
| Longitudinal emittance | eV.s | 1.0 | 1.0 |
| Normalised transverse emittance | μm.rad | 3.5 | 3.75 |
| Derived parameters | Unit | Injection | Collision |
| Protons per beam |  | 1.72 1012 |
| Current per beam |  | 3.1 |
| Stored energy per beam | MJ | .12 | .12 |
| Relativistic Gamma |  | 480 | 480 |
| Bunch length | cm | 11.24 | 11.24 |
| Beam size 1 & 5 | μm | 283 | 293 |
| Beam size 2 & 8 | μm | 270 | 280 |
| F |  | - | 1 |
| Peak luminosity 1 & 5 | cm-2 s-1 | - | 7.16 1028 |
| Events per crossing 1 & 5 (60mbarn) |  | - | 0.01 |

| Target machine parameters - Stage I - 43 bunch operation |
| --- |
| Set parameters | Unit | Injection | Collision |
| Crossing angle 1 & 5 | μrad | 0 | 0 |
| Crossing angle 2 | μrad | 0 | 0 |
| Crossing angle 8 | μrad | 0 | 0 |
| Separation 1 & 5 | mm | 5 | 5 |
| Separation 2 | mm | 4 | 4 |
| Separation 8 | mm | 4 | 4 |
| Beta * 1 & 5 | m | 11 | 2 |
| Beta * 2 & 8 | m | 10 | 10 |
| Crossing plane 1 |  | - |
| Crossing plane 2 |  | - |
| Crossing plane 5 |  | - |
| Crossing plane 8 |  | - |
| Energy | TeV | .450 | 7 |
| Number of bunches |  | 43 |
| Bunch intensity |  | 4 1010 |
| Longitudinal emittance | eV.s | 1.0 | 2.5 |
| Normalised transverse emittance | μm.rad | 3.5 | 3.75 |
| Derived parameters | Unit | Injection | Collision |
| Protons per beam |  | 1.72 1012 |
| Current per beam |  | 3.1 |
| Stored energy per beam | MJ | .12 | 1.9 |
| Relativistic Gamma |  | 480 | 7461 |
| Bunch length | cm | 11.24 | 7.55 |
| Beam size 1 & 5 | μm | 283 | 31.7 |
| Beam size 2 & 8 | μm | 270 | 70.9 |
| F |  | - | 1 |
| Peak luminosity 1 & 5 | cm-2 s-1 | - | 6.1 1030 |
| Events per crossing 1 & 5 (60mbarn) |  | - | 0.76 |

| Target machine parameters - Stage II - 75ns operation |
| --- |
| Set parameters | Unit | Injection | Collision |
| Crossing angle 1 & 5 | μrad | 320 | 250 |
| Crossing angle 2 | μrad | 480 | 300 |
| Crossing angle 8 | μrad | 600 | 400 |
| Separation 1 & 5 | mm | 5 | 5 |
| Separation 2 | mm | 4 | 4 |
| Separation 8 | mm | 4 | 4 |
| Beta * 1 & 5 | m | 11 | 2 |
| Beta * 2 & 8 | m | 10 | 10 |
| Crossing plane 1 |  | Vertical |
| Crossing plane 2 |  | Vertical |
| Crossing plane 5 |  | Horizontal |
| Crossing plane 8 |  | Horizontal |
| Energy | TeV | .450 | 7 |
| Number of bunches |  | 936 |
| Bunch intensity |  | 4 1010 |
| Longitudinal emittance | eV.s | 1.0 | 2.5 |
| Normalised transverse emittance | μm.rad | 3.5 | 3.75 |
| Derived parameters | Unit | Injection | Collision |
| Protons per beam |  | 3.74 1013 |
| Current per beam |  | 67.4 |
| Stored energy per beam | MJ | 0.12 | 42 |
| Relativistic Gamma |  | 480 | 7461 |
| Bunch length | cm | 11.24 | 7.55 |
| Beam size 1 & 5 | μm | 283 | 31.7 |
| Beam size 2 & 8 | μm | 270 | 70.9 |
| F |  | - | 0.96 |
| Peak luminosity 1 & 5 | cm-2 s-1 | - | 1.28 1032 |
| Events per crossing 1 & 5 (60mbarn) |  | - | 0.73 |

| Target machine parameters - Stage III - 25ns operation - Phase 1 collimators |
| --- |
| Set parameters | Unit | Injection | Collision |
| Crossing angle 1 & 5 | μrad | 320 | 285 |
| Crossing angle 2 | μrad | 480 | 300 |
| Crossing angle 8 | μrad | 600 | 400 |
| Separation 1 & 5 | mm | 5 | 0 |
| Separation 2 | mm | 4 | 0 |
| Separation 8 | mm | 4 | 0 |
| Beta * 1 & 5 | m | 11 | 1 |
| Beta * 2 & 8 | m | 10 | 1 - 50 |
| Crossing plane 1 |  | Vertical |
| Crossing plane 2 |  | Vertical |
| Crossing plane 5 |  | Horizontal |
| Crossing plane 8 |  | Horizontal |
| Energy | TeV | .45 | 7 |
| Number of bunches |  | 2808 |
| Bunch intensity |  | 5 1010 |
| Longitudinal emittance | eV.s | 1.0 | 2.5 |
| Normalised transverse emittance | μm.rad | 3.5 | 3.75 |
| Derived parameters | Unit | Injection | Collision |
| Protons per beam |  | 1.4 1014 |
| Current per beam |  | 253 |
| Stored energy per beam | MJ | 10 | 157 |
| Relativistic Gamma |  | 480 | 7461 |
| Bunch length | cm | 11.24 | 7.55 |
| Beam size 1 & 5 | μm | 283 | 22.4 |
| Beam size 2 & 8 | μm | 270 | 70.9 |
| F |  | - | 0.90 |
| Peak luminosity 1 & 5 | cm-2 s-1 | - | 1.13 1033 |
| Events per crossing 1 & 5 (60mbarn) |  | - | 2.1 |

| Target machine parameters - Stage IV - 25ns operation - Phase 2 collimators |
| --- |
| Set parameters | Unit | Injection | Collision |
| Crossing angle 1 & 5 | μrad | 320 | 285 |
| Crossing angle 2 | μrad | 480 | 300 |
| Crossing angle 8 | μrad | 600 | 400 |
| Separation 1 & 5 | mm | 5 | 0 |
| Separation 2 | mm | 4 | 0 |
| Separation 8 | mm | 4 | 0 |
| Beta * 1 & 5 | m | 11 | 1 |
| Beta * 2 & 8 | m | 10 | 1 - 50 |
| Crossing plane 1 |  | Vertical |
| Crossing plane 2 |  | Vertical |
| Crossing plane 5 |  | Horizontal |
| Crossing plane 8 |  | Horizontal |
| Energy | TeV | .45 | 7 |
| Number of bunches |  | 2808 |
| Bunch intensity |  | 9 1010 |
| Longitudinal emittance | eV.s | 1.0 | 2.5 |
| Normalised transverse emittance | μm.rad | 3.5 | 3.75 |
| Derived parameters | Unit | Injection | Collision |
| Protons per beam |  | 2.53 1014 |
| Current per beam |  | 455 |
| Stored energy per beam | MJ | 18 | 283 |
| Relativistic Gamma |  | 480 | 7461 |
| Bunch length | cm | 11.24 | 7.55 |
| Beam size 1 & 5 | μm | 283 | 22.4 |
| Beam size 2 & 8 | μm | 270 | 70.9 |
| F |  | - | 0.90 |
| Peak luminosity 1 & 5 | cm-2 s-1 | - | 3.65 1033 |
| Events per crossing 1 & 5 (60mbarn) |  | - | 6.9 |

| Target machine parameters - Nominal |
| --- |
| Set parameters | Unit | Injection | Collision |
| Crossing angle 1 & 5 | μrad | 320 | 285 |
| Crossing angle 2 | μrad | 480 | 300 |
| Crossing angle 8 | μrad | 600 | 400 |
| Separation 1 & 5 | mm | 5 | 0 |
| Separation 2 | mm | 4 | 0 |
| Separation 8 | mm | 4 | 0 |
| Beta * 1 & 5 | m | 11 | .55 |
| Beta * 2 & 8 | m | 10 | 1 - 50 |
| Crossing plane 1 |  | Vertical |
| Crossing plane 2 |  | Vertical |
| Crossing plane 5 |  | Horizontal |
| Crossing plane 8 |  | Horizontal |
| Energy | TeV | .45 | 7 |
| Number of bunches |  | 2808 |
| Bunch intensity |  | 1.15 1011 |
| Longitudinal emittance | eV.s | 1.0 | 2.5 |
| Normalised transverse emittance | μm.rad | 3.5 | 3.75 |
| Derived parameters | Unit | Injection | Collision |
| Protons per beam |  | 3.23 1014 |
| Current per beam |  | 581 |
| Stored energy per beam | MJ | 23 | 362 |
| Relativistic Gamma |  | 480 | 7461 |
| Bunch length | cm | 11.24 | 7.55 |
| Beam size 1 & 5 | μm | 283 | 16.7 |
| Beam size 2 & 8 | μm | 270 | 70.9 |
| F |  | - | 0.84 |
| Peak luminosity 1 & 5 | cm-2 s-1 | - | 1.01 1034 |
| Events per crossing 1 & 5 (60mbarn) |  | - | 19.2 |

Tolerances - from design report

| Tolerances - Nominal |
| --- |
| Set parameters | Unit | Injection | Collision |
| Horizontal tune |  | 64.28 | 64.31 |
| Vertical tune |  | 59.31 | 59.32 |
| Chromaticity |  | 2 | 2 |
| Tolerances |  |  |  |
| Bunch to bunch intensity | % |  | 10 |
| Bunch to bunch transverse emittance | % |  | 20 |
| Orbit (IP) | mm |  | 10% beam size |
| Crossing (IP) | mm |  | 10% crossing |
| Tune |  |  | 3 10-3 |
| Coupling |  |  | .001 |
| Chromaticity |  |  | 2 |
| Orbit (global) | mm |  | 4 |
| Orbit (local) |  |  | 0.1σ |
| Beta beat |  |  | 20% |
| Dispersion (spurious/normalized) |  |  | 27% |

Tolerances - from Frank’s presentation at the 19th LHCCWG

|  | 2007 com. | nominal | effect/reason |
| --- | --- | --- | --- |
| peak closed orbit | ? | 4 (3) mm [2] | mechanical aperture |
| rms closed orbit | ? | 0.40 mm [2] | feed down, dynamic aperture |
| orbit stability | ? | 0.2 s (0.6 s [6,13]) | arc beam losses, collimation |
| static off-momentum (1.5x10-3) peak bbeat | ? | 21% [1,2,3] | aperture, collimation |
| transient peak b beat | ? | <8% [6,13] | arc beam losses, collimation, aperture |
| peak dispersion D/√β | ? | 27% [4] | collimation, aperture |
| coupling k | ? | 0.001 [7,8] | tune control, diag. |
| tune | ? | 0.003/0.001 [7] | stable tune region, & tune spread |
| d deviation | ? | 1.5x10-3[2] 2x10-3[7] | aperture, collimation |
| stability | ? | 10-4 [8] | rf capture, HERA |
| dynamic aperture | ? | 6 (10-12) s [2] | lifetime, beam control |

|  | 2007 com. | nominal | effect/reason |
| --- | --- | --- | --- |
| chromaticity Q’ | 5±5 [5,7] | 2±1 [7] | instabilities, dyn. ap. |
| 2nd order Q’’ | few 1000 | 1000/2000 [2] | head-tail stability for Q’ meas., DQ |
| 3rd order Q’’ | 3x106? | >-5x105 [7,9], <3x106 | head-tail stability, dyn. aperture, DQ |
| detuning/amplitude@6s | 0.005? | 0.002 [7] | dynamic aperture, DQ |
| ∂2Q/(∂e)/(∂d) | ? | 7x106 m-1 [2] | total tune spread DQ |
| bunch-to-bunch intensity | ? | ±10% peak [11] | PS booster rings, PS |
| bunch-to-bunch transv. emittance variation | ? | ±10% peak [11] | PS booster rings, PS |
| bunch-to-bunch longit. emittance variation | ? | ±10% peak [11] +0/-10% [12] | PS booster rings, PS |
| minimum / maximum transverse emittance | ? | 3 mm<e <3.75mm | beam-beam, collimator survival, aperture |
| vacuum beam lifetime | 1 (30?) h ? | 100 h [10] | nuclear interaction |